## Slide 1
1. ENTERPRISE ARCHITECTURE • GENERAL ELECTRIC
SAP S/4HANA & MES Clean-Core Decoupled Architecture
Preserving ERP financial ledger integrity via event-driven edge execution.
General Electric • Enterprise Architecture Blueprint • Systems-Thinking Guardrails
01 / 01
ISA-95 LEVEL 4
ENTERPRISE / ERP
ZONE: Corporate Cloud (AWS/GCP)
SAP S/4HANA Core
Financial & Order Ledger
Production Orders • BOM / Routing
DATA STORE
SAP HANA Cloud DB
HANA Columnar
Enterprise PLM
Engineering Master Data
INTERFACE: OData v4 & SAP Event Mesh
[TLS 1.3 Async] PAYLOAD: ProductionOrder_v2, MaterialMaster (MARA)
BTP INTEGRATION
INTEGRATION MIDDLEWARE
ZONE: Cloud DMZ / Proxy
SAP BTP Integration Suite
API Mediation & Policy
Enterprise Event Mesh
Pub/Sub Event Broker
GoodsIssue Event • OrderStatus
API / ENDPOINT
API Gateway & Security
INTERFACE: HTTPS / REST & WebSocket
[Bi-Directional Sync] PAYLOAD: DispatchOrderPayload, OperationStepList
ISA-95 LEVEL 3
MANUFACTURING MOM / MES
ZONE: Plant Local LAN
SAP Digital Manufacturing (DMC)
Work Order Dispatcher & POD
WIP Tracking • Non-Conformance
DATA STORE
Plant Operational DB
PostgreSQL Timescale
Quality & Yield Engine
SPC & Tolerance Limits
INTERFACE: OPC UA (Binary) & MQTT
[Air-Gapped Gateway] PAYLOAD: WorkCenterDispatch, ToolParameters, BatchID
ISA-95 LEVEL 2
INDUSTRIAL EDGE & CONNECTIVITY
ZONE: Industrial Edge IPC
Edge Runtime Gateway
Local Buffer & Protocol Conv
48h Offline Buffer
API / ENDPOINT
Kepware / OPC UA Server
DATA STORE
Edge Cache DB
SQLite / Edge Disk
INTERFACE: PROFINET & Fieldbus I/O
[Sub-100ms Deterministic] PAYLOAD: MachineSpeed, SpindleTemp, CycleCount, InterlockSignal
ISA-95 LEVEL 1 / 0
SHOP FLOOR EXECUTION
ZONE: Isolated OT Machine Subnet
DEVICE / OT
Siemens S7-1500 PLC
Cell Automation & Interlocks
DEVICE / OT
DMG 5-Axis CNC Spindle
Precision Machining Center
DEVICE / OT
Cognex Vision Camera
Automated Optical Inspection
OPERATOR
Line Assembly Operator
ARCHITECTURAL GUARANTEES
• SINGLE FINANCIAL LEDGER
S/4HANA ACDOCA remains the sole financial source of truth. MES never replicates general ledger postings.
• AIR-GAPPED PLANT RESILIENCE
Edge gateways buffer 48 hours of telemetry and execution confirmations during WAN network disconnects.
• CLEAN-CORE DECOUPLING
Zero custom ABAP modifications in S/4HANA core. All MES orchestrations leverage standard OData v4 and Event Mesh.
• DETERMINISTIC MACHINE INTERLOCK
Sub-100ms machine safety and cycle interlocks run exclusively at Level 1/2 PLC layer, immune to cloud latency.

## Slide 2
2. OPERATIONAL SWIMLANE
Cross-Functional SAP, MES & Shop Floor Handoff Architecture
End-to-end transactional handoffs with Poka-Yoke error-proofing interlocks.
General Electric • Operational Swimlane Advisory
02 / 05
CROSS-FUNCTIONAL OPERATIONAL SWIMLANE: ORDER-TO-CONFIRMATION OPERATIONAL SWIMLANE
CUSTOMER DEMAND
External Partner
SAP S/4HANA
System of Record
MES MOM CORE
Execution
SHOP FLOOR / OT
Edge Physical Layer
QUALITY ASSURANCE
Compliance Interlock
[1] EDI 850
Demand Forecast / EDI
Sales Demand Signal
[2] S/4HANA PP
Sales & Production Order
MRP Planning Run
[3] MES MOM
Dispatch & Work Queue
Operation Scheduling
[4] PLC / OPC UA
CNC Machining & Setup
Physical Execution
[5] 261 Movement
Material Consumption
Batch Component Binding
[6] CMM Gauge
Optical Inspection Gate
SPC Tolerance Validation
[7] ACDOCA Post
Confirmation & Ledger
CO11N & 101 Goods Receipt
Sales Order
Production Order
Dispatch Job
Inspection Trigger
Clearance GR

## Slide 3
3. PROCESS EXECUTION
Production Execution, Quality Clearance & Rework Loopback
Sequential order dispatch with automated Poka-Yoke decision gate and rework loopback.
General Electric • Production Execution Flow
03 / 05
PROCESS ARCHITECTURE: PRODUCTION EXECUTION & QUALITY CLEARANCE
STEP 1: CUSTOMER DEMAND
Demand & Sales Order
[SAP SD]
STEP 2: SAP CORE
Production Order & MRP
[PP Order 100482]
STEP 3: MES OPERATIONS
MES Dispatch & Setup
[Digital Dispatch]
STEP 4: SHOP FLOOR OT
Machine Execution
[CNC Work Center]
DECISION GATE
Quality Gate & SPC
PASS
STEP 6: SAP FINANCE
Confirmation & Ledger
[CO11N / 101 GR]
STEP 7: LOGISTICS
Finished Goods Dispatch
[Outbound Delivery]
REWORK
EXCEPTION PATH
Rework Operation
[MES Non-Conformance]
Quarantine & Root Cause Correction
LOCK: Defect Logged in S/4HANA QM
CLEARANCE GATE
Re-Inspection & Verification
[Digital Traveler]
Tolerance Validation & Clearance
LOCK: Serial Unlocked Only on Clearance
CLOSED-LOOP RE-ENTRY Cleared for Confirmation

## Slide 4
4. TRANSFORMATION BLUEPRINT
Current State to Future Operating Model Transformation Bridge
Bridging legacy operational friction through S/4HANA clean-core and MES execution enablers.
General Electric • Transformation Bridge
04 / 05
ENTERPRISE TRANSFORMATION BLUEPRINT: SAP TO MES DIGITAL TRANSFORMATION BLUEPRINT
CURRENT STATE (BASELINE)
Operational Constraints & Friction
✗ Fragmented master data & BOM mismatches
✗ Manual paper travelers & dispatch clipboards
✗ Disconnected quality logs in Excel
✗ Delayed inventory confirmation (2-3 day lag)
BASELINE METRICS
• WIP Latency: 4.8 Days
• Scrap Rate: 4.2%
• OTIF Delivery: 81.4%
TRANSFORMATION ENABLERS
Strategic Initiatives & Technology
⚙ SAP S/4HANA Clean-Core Integration
⚙ MES Digital Dispatch & Real-Time Tracking
⚙ Automated Closed-Loop Quality Interlocks
⚙ Unified Industrial Data Fabric & BTP Mesh
ENABLERS & ARCHITECTURE
✔ Air-gapped edge buffering
✔ Deterministic PLC connectors
✔ Zero custom Z-tables in ERP
FUTURE OPERATING MODEL
Transformed Capabilities
✔ Synchronized MRP-to-machine dispatch
✔ Full serial & batch genealogy trace
✔ Predictive quality interlocks at station
✔ Sub-second financial ledger postings
MEASURABLE OUTCOMES
★ WIP Latency: 1.2 Days (-75%)
★ Scrap Rate: 0.8% (-81%)
★ OTIF Delivery: 97.5% (+16 pts)
HORIZON: 12–18 MONTH EXECUTION HORIZON
Phase 1: S/4HANA Core & Clean Master Data ➔ Phase 2: MES MOM Dispatch & Traceability ➔ Phase 3: Closed-Loop Analytics & Autonomous Control

## Slide 5
5. MATURITY ASSESSMENT
Digital Transformation Maturity Staircase & Gap Scorecard
5-Level capability staircase and prioritized dimension gap scorecard.
General Electric • Maturity Assessment
05 / 05
DIGITAL TRANSFORMATION MATURITY ASSESSMENT: MANUFACTURING DIGITAL TRANSFORMATION MATURITY
TARGET: 4.2 / 5.0
CURRENT: 2.4 / 5.0
5-LEVEL DIGITAL MATURITY STAIRCASE
1. Fragmented
2. Standardized
[CURRENT POSITION]
3. Integrated
4. Intelligent
[TARGET HORIZON]
5. Autonomous
GAP AUDIT & PRIORITY INTERVENTIONS (SCORE -> GAP -> ACTION)
Process & Execution [P1]
Current: 2.1 / 5.0 ➔ Target: 4.3 / 5.0 (Gap: +2.2)
Gap: Paper travel cards & manual dispatch
Intervention: Deploy MES automated dispatch & digital traveler
Data & Genealogy [P1]
Current: 2.3 / 5.0 ➔ Target: 4.5 / 5.0 (Gap: +2.2)
Gap: Missing component-to-serial batch linkage
Intervention: Automated barcode & OPC-UA genealogy binding
SAP Clean Core [P2]
Current: 2.6 / 5.0 ➔ Target: 4.2 / 5.0 (Gap: +1.6)
Gap: Excess custom Z-tables blocking cloud upgrade
Intervention: Migrate custom code to BTP event mesh
Quality & Rework [P1]
Current: 2.2 / 5.0 ➔ Target: 4.0 / 5.0 (Gap: +1.8)
Gap: Delayed defect logging & missing CAPA loops
Intervention: Closed-loop digital inspection interlocks
Governance & RACI [P2]
Current: 2.8 / 5.0 ➔ Target: 4.0 / 5.0 (Gap: +1.2)
Gap: Ambiguous IT/OT boundary ownership
Intervention: Formalize unified IT/OT operating charter